ZLAC8015D Servo Hub Motor Driver
RS485 communication description

1. RS485 serial port settings
RS485 of ZLAC8015D supports Modbus RTU protocol.
The drive address can be set from 0-127, the default is 1;
7 kinds of baud rates, such as 9600, 19200, 38400, 57600, 115200, 128000, 256000, etc.
It can be set by software, the default is 115200;
Data bits 8, no parity, stop bit 1.

2. Protocol format
The MODBUS protocol defines a protocol data unit (PDU) independent of the underlying communication layer. specific bus
Or the MODBUS protocol mapping on the network can introduce some additional fields on the Application Data Unit (ADU).

The MODBUS protocol defines three PDUs:
MODBUS request PDU = {function code + request data field}
MODBUS response PDU = {function code + response data field}
MODBUS abnormal response PDU = {abnormal function code + error code}
The function codes supported by ZLAC8015 are as follows:

The function codes supported by ZLAC8015 are as follows:
Function description	function code	abnormal function code
read multiple registers	0x03	0x83
write a single register	0x06	0x86
write multiple registers	0x10	0x90

The error codes are as follows:
error code	name	Meaning
0x01	Illegal function code	Function code error
0x02	illegal data address	data address error
0x03	illegal data value	data error

2.1. Read register function code 0x03

Example: Send "Read Motor Actual Speed", return "Motor Actual Speed 10RPM"
Send
Command	Content description
01	drive address
03	function code
20	Register start address upper eight bits
AB	Register start address lower eight bits
00	The high eight bits of the number of registers
02	The lower eight bits of the number of registers
BE	CRC check upper eight bits
2B	CRC check low eight bits

return data
Command	Content description
01	drive address
03	function code
04	Read the number of data bytes
00	Data 0 high eight bits
64	Data 0 lower eight bits
00	Data 1 upper eight bits
64	Data 1 lower eight bits
BA	CRC check upper eight bits
07	CRC check low eight bits

2.2 Write a single register function code 0x06

Example: write left motor target speed 100RPM
send
Command	Content description
01	drive address
06	function code
20	Register start address upper eight bits
88	Register start address lower eight bits
00	Data high eight
64	Data lower eight bits
03	CRC check upper eight bits
CB	CRC check low eight bits

return data
Command	Content description
01	drive address
06	function code
20	Register start address upper eight bits
88	Register start address lower eight bits
00	Data high eight
64	Data lower eight bits
03	CRC check upper eight bits
CB	CRC check low eight bits

2.3 Write multiple registers function code 0x10

Example: write left motor encoder line number 1024, hall offset angle 0
send
Command	Content description
01	drive address
10	function code
20	Register start address upper eight bits
30	Register start address lower eight bits
00	The high eight bits of the number of registers
02	The lower eight bits of the number of registers
04	number of data bytes
04	Data 0 high eight bits
00	Data 0 lower eight bits
00	Data 1 upper eight bits
00	Data 1 lower eight bits
68	CRC check upper eight bits
4A	CRC check low eight bits

return data
Command	Content description
01	drive address
10	function code
20	Register start address upper eight bits
30	Register start address lower eight bits
02	The high eight bits of the number of registers
4A	The lower eight bits of the number of registers
07	CRC check upper eight bits
01	CRC check low eight bits

3. Control routine
3.1 Speed Mode
The relevant parameter addresses are as follows:
Index	Name	instruction	type	property	Default
200Eh	control word	control word / 0x05: Emergency stop / 0x06: Alarm clear / 0x07: Downtime / 0x08: enable	U16	RW	0
200Dh	operating mode	3: speed mode;	U16	RW	0
2080h	S-shaped acceleration time (left motor)	acceleration time; / Range: 0-32767ms;	U16	RW	500ms
2081h	S-shaped acceleration time (right motor)	acceleration time; / Range: 0-32767ms;	U16	RW	500ms
2082h	S-shaped deceleration time (left motor)	deceleration time; / Range: 0-32767ms;	U16	RW	500ms
2083h	S-shaped deceleration time (right motor)	deceleration time; / Range: 0-32767ms;	U16	RW	500ms
2088h	Left motor target speed	target speed in speed mode; / Range: -3000-3000r/min;	I16	RW	0
2089h	Right motor target speed	target speed in speed mode; / Range: -3000-3000r/min;	I16	RW	0
20ABh	Actual speed feedback (left)	The current motion speed of the motor, the unit is 0.1r/min	I16	RO	0
20ACh	Actual speed feedback (right)	The current motion speed of the motor, the unit is 0.1r/min	I16	RO	0

Speed mode initialization
instruction	send	recv
Set speed mode	01 06 20 0D 00 03 53 C8	01 06 20 0D 00 03 53 C8
Set the left motor / S-type acceleration time 500ms	01 06 20 80 01 F4 83 F5	01 06 20 80 01 F4 83 F5
Set the right motor / S-type acceleration time 500ms	01 06 20 81 01 F4 D2 35	01 06 20 81 01 F4 D2 35
Set the left motor / S-type deceleration time 500ms	01 06 20 82 01 F4 22 35	01 06 20 82 01 F4 22 35
Set the right motor / S-type deceleration time 500ms	01 06 20 83 01 F4 73 F5	01 06 20 83 01 F4 73 F5
Enable	01 06 20 0E 00 08 E2 0F	01 06 20 0E 00 08 E2 0F

Left motor speed control
instruction	send	recv
Set the left motor / Target speed 100RPM	01 06 20 88 00 64 03 CB	01 06 20 88 00 64 03 CB
Set the left motor / Target speed-100RPM	01 06 20 88 FF 9C 43 B9	01 06 20 88 FF 9C 43 B9
downtime	01 06 20 31 00 07 92 07	01 06 20 31 00 07 92 07

Right motor speed control
instruction	send	recv
Set the right motor / Target speed 100RPM	01 06 20 89 00 64 52 0B	01 06 20 89 00 64 52 0B
Set the right motor / Target speed-100RPM	01 06 20 89 FF 9C 12 79	01 06 20 89 FF 9C 12 79
downtime	01 06 20 31 00 07 92 07	01 06 20 31 00 07 92 07

Synchronous speed control
instruction	send	recv
set sync / Target speed 100RPM	01 10 20 88 00 02 04 00 64 00 64 23 9C	01 10 20 88 00 02 CA 22
set sync / Target speed-100RPM	01 10 20 88 00 02 04 FF 9C FF 9C D2 0B	01 10 20 88 00 02 CA 22
downtime	01 06 20 31 00 07 92 07	01 06 20 31 00 07 92 07

3.2 Position Mode
The relevant parameter addresses are as follows:
index	name	instruction	Type	Property	Default
200Eh	control word	control word / 0x05: Emergency stop / 0x06: Alarm clear / 0x07: Downtime / 0x08: enable / 0x10: start (sync) (position mode / required below) / 0x11: Start (left motor) / 0x12: start (right motor)	U16	RW	0
200Fh	Synchronous/Asynchronous Control Flag	0: Asynchronous control / 1: Synchronous control	U16	RW	0
200Dh	operating mode	1: position mode (relative position mode); / 2: position mode (absolute position mode);	U16	RW	0
2080h	Left motor S-curve acceleration time	acceleration time; / Range: 0-32767ms;	U16	RW	500ms
2081h	Right motor S-curve acceleration time	acceleration time; / Range: 0-32767ms;	U16	RW	500ms
2082h	Left motor S-curve deceleration time	deceleration time; / Range: 0-32767ms;	U16	RW	500ms
2083h	Right motor S-curve deceleration time	deceleration time; / Range: 0-32767ms;	U16	RW	500ms
208Ah	Left motor target position high 16 bit	The range of the total number of pulses in position mode operation: / Relative: -0x7FFFFFFF~0x7FFFFFFF; / absolute: -0x3FFFFFFF~0x3FFFFFFF;	I16	RW	0
208Bh	Left motor target position low 16 / bit		I16	RW	0
208Ch	Right motor target position high 16 / bit	The range of the total number of pulses in position mode operation: / Relative: -0x7FFFFFFF~0x7FFFFFFF; / absolute: -0x3FFFFFFF~0x3FFFFFFF;	I16	RW	0
208Dh	Right motor target position low 16 / bit		I16	RW	0
208Eh	Left motor maximum speed	Maximum speed in position mode; / Range: 1-1000r/min;	U16	RW	120r/min
208Fh	Right motor maximum speed	Maximum speed in position mode; / Range: 1-1000r/min;	U16	RW	120r/min
20A7h	Actual position feedback position high / 16 bit (left)	Actual position feedback, unit counts; / -0x7FFFFFFF~0x7FFFFFFFF;	I16	RO	0
20A8h	Actual position feedback position low / 16 bit (left)		I16	RO	0
20A9h	Actual position feedback position high / 16 bit (right)	Actual position feedback, unit counts; / -0x7FFFFFFF~0x7FFFFFFFF;	I16	RO	0
20AAh	Actual position feedback position low / 16 bit (right)		I16	RO	0

Position mode asynchronous control initialization
instruction	send	recv
Set up asynchronous control	01 06 20 0F 00 00 B2 09
Set relative position mode	01 06 20 0D 00 01 D2 09
Set the left motor / S-type acceleration time 500ms	01 06 20 80 01 F4 83 F5	01 06 20 80 01 F4 83 F5
Set the right motor / S-type acceleration time 500ms	01 06 20 81 01 F4 D2 35	01 06 20 81 01 F4 D2 35
Set the left motor / S-type deceleration time 500ms	01 06 20 82 01 F4 22 35	01 06 20 82 01 F4 22 35
Set the right motor / S-type deceleration time 500ms	01 06 20 83 01 F4 73 F5	01 06 20 83 01 F4 73 F5
Set the left motor Maximum speed 50RPM	01 06 20 8E 00 32 63 F4	01 06 20 8E 00 32 63 F4
Set the right motor / Maximum speed 50RPM	01 06 20 8F 00 32 32 34	01 06 20 8F 00 32 32 34
Enable	01 06 20 0E 00 08 E2 0F	01 06 20 0E 00 08 E2 0F

Left motor relative position control
instruction	send	recv
Set the left motor / Target position 20480pulses	01 10 20 8A 00 02 04 00 00 50 00 DE 71	01 10 20 8A 00 02 6B E2
left motor start	01 06 20 0E 00 11 23 C5	01 06 20 0E 00 11 23 C5
Set the left motor / target location - 20480pulses	01 10 20 8A 00 02 04 FF FF B0 00 97 95	01 10 20 8A 00 02 6B E2
left motor start	01 06 20 0E 00 11 23 C5	01 06 20 0E 00 11 23 C5
downtime	01 06 20 0E 00 07 A2 0B	01 06 20 0E 00 07 A2 0B

Right motor relative position control
instruction	send	recv
Set the right motor / Target position 20480pulses	01 10 20 8C 00 02 04 00 00 50 00 5E 5B	01 10 20 8C 00 02 8B E3
Right motor starts	01 06 20 0E 00 11 23 C501 06 20 0E 00 12 63 C4	01 06 20 0E 00 12 63 C4
Set the right motor / target location - 20480pulses	01 10 20 8C 00 02 04 FF FF B0 00 17 BF	01 10 20 8C 00 02 8B E3
Right motor starts	01 06 20 0E 00 12 63 C4	01 06 20 0E 00 12 63 C4
downtime	01 06 20 0E 00 07 A2 0B	01 06 20 0E 00 07 A2 0B

Position mode synchronization control initialization
instruction	send	recv
Set up sync control	01 06 20 0F 00 01 73 C9	01 06 20 0F 00 01 73 C9
Set relative position mode	01 06 20 0D 00 01 D2 09	01 06 20 0D 00 01 D2 09
Set the left motor / S-type acceleration time 500ms	01 06 20 80 01 F4 83 F5	01 06 20 80 01 F4 83 F5
Set the right motor / S-type acceleration time 500ms	01 06 20 81 01 F4 D2 35	01 06 20 81 01 F4 D2 35
Set the left motor / S-type deceleration time 500ms	01 06 20 82 01 F4 22 35	01 06 20 82 01 F4 22 35
Set the right motor / S-type deceleration time 500ms	01 06 20 83 01 F4 73 F5	01 06 20 83 01 F4 73 F5
Set the left motor / Maximum speed 50RPM	01 06 20 8E 00 32 63 F4	01 06 20 8E 00 32 63 F4
Set the right motor / Maximum speed 50RPM	01 06 20 8F 00 32 32 34	01 06 20 8F 00 32 32 34
Enable	01 06 20 0E 00 08 E2 0F	01 06 20 0E 00 08 E2 0F

Synchronized relative position control
instruction	send	recv
set sync / Target position 20480pulses	01 10 20 8A 00 04 08 00 00 50 00 00 00 50 00 E3 2C	01 10 20 8A 00 04 EB E0
start up	01 06 20 0E 00 10 E2 05	01 06 20 0E 00 10 E2 05
set sync / target location - 20480pulses	01 10 20 8A 00 04 08 FF FF B0 00 FF FF B0 00 FC A3	01 10 20 8A 00 04 EB E0
start up	01 06 20 0E 00 10 E2 05	01 06 20 0E 00 10 E2 05
downtime	01 06 20 0E 00 07 A2 0B	01 06 20 0E 00 07 A2 0B

3.3 Torque Mode

The relevant parameter addresses are as follows:
index	name	instruction	type	Attributes	Defaults
200Eh	control word	control word / 0x05: Emergency stop / 0x06: Alarm clear / 0x07: Downtime / 0x08: enable	U16	RW	0
200Dh	operating mode	4: Torque mode;	U16	RW	0
2086h	Left motor torque slope	current/1000/second; / Unit: mA/S;	U16	RW	300ms
2087h	Right motor torque slope	current/1000/second; / Unit: mA/S;	U16	RW	300ms
2090h	Left motor target torque	Unit: mA / Range: -30000~30000;	I16	RW	0
2091h	Right motor target torque	Unit: mA / Range: -30000~30000;	I16	RW	0
20ADh	Real-time torque feedback (left)	Unit: 0.1A / Range: -300~300;	I16	RO	0
20AEh	Real-time torque feedback (right)	Unit: 0.1A / Range: -300~300;	I16	RO	0

Torque mode initialization
instruction	send	recv
Set torque mode	01 06 20 0D 00 04 12 0A	01 06 20 0D 00 04 12 0A
Set the left motor / Torque slope 500mA/s	01 06 20 86 01 F4 63 F4	01 06 20 86 01 F4 63 F4
Set the right motor / Torque slope 500mA/s	01 06 20 87 01 F4 32 34	01 06 20 87 01 F4 32 34
motor enable	01 06 20 31 00 08 D2 03	01 06 20 31 00 08 D2 03

Left motor torque control
instruction	send	recv
Set the left motor / Target torque 2000mA	01 06 20 90 07 D0 81 8B	01 06 20 90 07 D0 81 8B
Set the left motor / Target torque -2000mA	01 06 20 90 F8 30 C1 F3	01 06 20 90 F8 30 C1 F3
downtime	01 06 20 0E 00 07 A2 0B	01 06 20 0E 00 07 A2 0B

Right motor torque control
instruction	send	recv
Set the right motor / Target torque 2000mA	01 06 20 91 07 D0 D0 4B	01 06 20 91 07 D0 D0 4B
Set the right motor / Target torque -2000mA	01 06 20 91 F8 30 90 33	01 06 20 91 F8 30 90 33
downtime	01 06 20 0E 00 07 A2 0B	01 06 20 0E 00 07 A2 0B

Synchronous torque control
instruction	send	recv
set sync / Target torque 2000mA	01 10 20 90 00 02 04 07 D0 07 D0 60 23	01 10 20 90 00 02 4A 25
set sync / Target torque -2000mA	01 10 20 90 00 02 04 F8 30 F8 30 11 B9	01 10 20 90 00 02 4A 25
downtime	01 06 20 0E 00 07 A2 0B	01 06 20 0E 00 07 A2 0B

3.5 Emergency stop command and external emergency stop
index	name	instruction	type	Attributes	default
200Eh	control word	0x05: Emergency stop / 0x06: Alarm clear / 0x07: Downtime / 0x08: enable / 0x10: start (required in position mode)	U16	RW	0
2016h	Input terminal effective level	Bit0: Control bit of input terminal X0; / Bit1: Input terminal X1 control bit; / 0: default; / 1: level inversion; / The driver defaults to the rising edge of the input terminal level or / Active high;	U16	RW/S	0
2017h	Input terminal X0 Terminal function selection	0: undefined; / 1-8: NC; / 9: Emergency stop signal;	U16	RW/S	9
2018h	Input terminal X1 terminal function / can choose		U16	RW/S	0

※Note: Please refer to the "ZLAC8015D Servo Hub Driver User Manual" for the external wiring diagram of the input port.

Emergency stop command:
instruction	send	recv
emergency stop	01 06 20 0E 00 05 23 CA	01 06 20 0E 00 05 23 CA

3.6 Troubleshooting and Clearing
ZLAC8015D supports overvoltage, overcurrent protection, etc. All fault information can be read through the address 0x20A5/0x20A6 (left/
right drive) to get

The fault codes are as follows:
0x603F	Function description
0x0000	no errors
0x0001	overvoltage
0x0002	undervoltage
0x0004	overcurrent
0x0008	overload
0x0010	Current out of tolerance
0x0020	Encoder out of tolerance
0x0040	Too bad
0x0080	reference voltage error
0x0100	EEPROM read and write errors
0x0200	Hall went wrong
0x0400	Motor temperature is too high

fault clearing
instruction	send	recv
clear fault	01 06 20 0E 00 06 63 CB	01 06 20 0E 00 06 63 CB

Appendix A Address Directory